-----***4 input NOR Gate(Q no:1)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Nor4 is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);------output
end Nor4;
----------------------------
architecture Operation of Nor4 is
begin
  o<= not(a or b or c or d);
end operation;

-----***4 input NAND Gate(Q no: 2)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Nand4 is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);--output
end Nand4;
----------------------------
architecture Operation of Nand4 is
begin
  o<= not(a and b and c and d);
end operation;

-----***3 input AND Gate(Q no:3)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity And3 is
  port(
    a,b,c:in std_logic;--inputs
    d:out std_logic);--output
end And3;
----------------------------
architecture Operation of And3 is
begin
  d<= a and b and c;
end operation;

-----***3 input Xor Gate(Q no:4)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Xor3 is
  port(
    a,b,c:in std_logic;--inputs
    o:out std_logic);--output
end Xor3;
----------------------------
architecture Operation of Xor3 is
begin
  o<= a xor b xor c;
end operation;

-----***2 input Ex-Nor Gate(Q no:5)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity XNor2 is
  port(
    a,b:in std_logic;--inputs
    o:out std_logic);--output
end XNor2;
----------------------------
architecture Operation of XNor2 is
begin
  o<= a xnor b;
end operation;

-----***3 input OR Gate(Q no:6)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Or3 is
  port(
    a,b,c:in std_logic;--inputs
    o:out std_logic);--output
end Or3;
----------------------------
architecture Operation of Or3 is
begin
  o<= a or b or c;
end operation;

-----***3 input NAND Gate(Q no:7)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
-----------------------------
entity Nan3 is
  port(
    a,b,c:in std_logic;--inputs
    o:out std_logic);--outputs
  end Nan3;
-----------------------------
  architecture operation of Nan3 is
  begin
    o<= not(a and b and c);
  end operation;

-----***3 input NOR Gate(Q no:9)***-----
-----coded by Jenson and Salahudheen-----

library ieee;
use ieee.std_logic_1164.all;
-----------------------------
entity Nor3 is
  port(
    a,b,c:in std_logic;--inputs
    d:out std_logic);--ouput
  end Nor3;
-----------------------------
  architecture Op of Nor3 is
  begin
    d<=(not(a or b or c));
  end op;

-----***Half Adder(Q no:10)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
-------------------------------
entity HalfAdder is

    port(

        a,b:in std_logic;--inputs
        sum,carry:out std_logic);--output

end HalfAdder;
-------------------------------

architecture Operation of HalfAdder is

  begin

    sum<=a xor b;
    carry<= a and b;

end Operation;

-----***Full Adder(Q no:11)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity FullAdder is
  port(

    a,b,cin:in std_logic;--inputs
    sum,carry:out std_logic);--output
end FullAdder;
----------------------------
architecture Operation of FullAdder is

    begin
      sum<= a xor b xor cin ;
      carry<= (a and b) or (a and cin) or (b and cin);
end Operation;

-----***2-1 Mux(Q no:12)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Mux is
  port(
    a,b,ce:in std_logic;--inputs
    cout:out std_logic);--output
end Mux;
----------------------------
architecture Operation of Mux is
begin
  cout<= ((not ce) and a) or(ce and b);
end Operation;

------***4-1 Mux(Q no:13)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Mux4 is
  port(
    a,b,c,d,ce1,ce2:in std_logic;--input
    cout:out std_logic);--output
  end Mux4;
-----------------------------
architecture Operation of Mux4 is
begin
  cout<= ((not ce1)and (not ce2)and a) or ((not ce1)and (ce2)and b) or ((ce1)and (not ce2)and c) or ((ce1)and (ce2)and d );
end Operation;

-----***8-1 Mux(Q no:14)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity Mux8x1 is
  port( a,b,c,d,e,f,g,h,s0,s1,s2 : in std_logic;--inputs&select
        out1 : out std_logic);--output
end Mux8x1;
--------------
architecture Operation of Mux8x1 is
begin
  out1<= (( not s0) and ( not s1) and (not s2) and a) or
   (( not s0) and (not s1) and s2 and b) or
   (( not s0) and ( s1) and (not s2) and c) or
   (( not s0) and ( s1) and ( s2) and d) or
   (( s0) and ( not s1) and (not s2) and e) or
   (( s0) and ( not s1) and ( s2) and f) or
   (( s0) and ( s1) and (not s2) and g) or
   (( s0) and ( s1) and ( s2) and h) ;
end Operation;

-----***16-1 Mux(Q no:15)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity mux16_1 is
  port( a,b,c,d,e,f,g,h,i,j,k,l,m,n,o,p,s0,s1,s2,s3 : in std_logic;--inputs&select
        out1 : out std_logic);--output
end mux16_1;
--------------------------------
architecture Operation of mux16_1 is
begin
  out1<= (( not s0) and ( not s1) and (not s2) and (not s3) and a) or
   (( not s0) and (not s1) and (not s2) and (s3) and b) or
   (( not s0) and (not s1) and (s2) and(not s3) and c) or
   (( not s0) and (not s1) and (s2) and (s3) and d) or
   (( not s0) and (s1) and (not s2) and (not s3) and e) or
   (( not s0) and (s1) and (not s2) and (s3) and f) or
   (( not s0) and (s1) and (s2) and(not s3) and g) or
   (( not s0) and (s1) and (s2) and (s3) and h) or
   ((s0) and (not s1) and (not s2) and (not s3) and i) or
   ((s0) and (not s1) and (not s2) and (s3) and j) or
   ((s0) and (not s1) and (s2) and (not s3) and k) or
   ((s0) and (not s1) and (s2) and (s3) and l) or
   ((s0) and (s1) and (not s2) and (not s3) and m) or
   ((s0) and (s1) and (not s2) and (s3) and n) or
   ((s0) and (s1) and (s2) and (not s3) and o) or
   ((s0) and (s1) and (s2) and (s3) and p);

 end Operation;

------***1-2 DeMux(Q no:16)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------------
entity dmux is
  port (a : in std_logic;--input
        s :in std_logic;--select
        o1,o2 : out std_logic);--output
end dmux;
---------------------------------
architecture Operation of dmux is
begin

 o2<= a and s;
 o1<= a and (not s);
  end Operation;

-----2-4 line Decoder(Q no:17)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity Demux4x2 is
  port(
    a,b,en:in std_logic;--inputs&select
    z : out std_logic_vector(3 downto 0));--output
end Demux4x2;
---------------------------------
architecture Operation of Demux4x2 is
signal abar,bbar:std_logic;
begin
  z(3)<=(a and b and en);
  z(0)<= (abar and bbar and en);
  bbar<=not b;
  z(2)<=(a and bbar and en);
  abar<=not a;
  z(1)<=(abar and b and en);
end Operation;

-----***Demux 8x1(Q no:18)***------------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
use ieee.std_logic_unsigned.all;
------------------------------------
entity Demux8x1 is
  port (
    input : in std_logic;
    sel : in std_logic_vector(2 downto 0);
    output : out std_logic_vector(7 downto 0));
end Demux8x1;
-------------------------------------
architecture Operation of Demux8x1 is
begin
  output(0) <= (not sel(2)) and (not sel(1)) and (not sel(0)) and input;
  output(1) <= (not sel(2)) and (not sel(1)) and sel(0) and input;
  output(2) <= (not sel(2)) and sel(1) and (not sel(0)) and input;
  output(3) <= (not sel(2)) and sel(1) and sel (0) and input;
  output(4) <= sel(2) and (not sel(1)) and (not sel (0)) and input;
  output(5) <= sel(2) and (not sel(1)) and sel (0) and input;
  output(6) <= sel(2) and sel(1) and (not sel (0)) and input;
  output(7) <= sel(2) and sel(1) and sel (0) and input;
end Operation;

------***MasterSlave JK FF(Q no:19)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity msjkff is
  port (j , k , out_pre : in std_logic;
        out_next : out std_logic);
end msjkff;

architecture Operation of msjkff is

begin

  out_next <= out_pre when j ='0' and k='0' else
        '1' when j ='1' and k='0' else
        '0'when j ='0' and k='1' else
        '-';
end Operation;

-----**RS NOR Latch(Q no:20)***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity rs_latch is
  port(r,s : in std_logic;
       q,qbar:inout std_logic);
end rs_latch;
---------------------------------
architecture Operation of rs_latch is
begin
  q <= s nor qbar;
  qbar <= r nor q;
end Operation;

-----***Realization (Q no:21)***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Realise1 is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);--output
end Realise1;
----------------------------
architecture Operation of Realise1 is
  begin
    o<=((a xnor b) and (c xnor d)) or ((a xor b) and (c xor d));
end operation;

-----***Realization (Q no:22(a))***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Realise2 is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);--output
end Realise2;
----------------------------
architecture Operation of Realise2 is
  begin
    o<= (((not d) or (b and c)) and (not a)) or ((a and d) and (not b));
end operation;

-----***Realisation (Q no:22(b))***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Realise2b is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);--output
end Realise2b;
----------------------------
architecture Operation of Realise2b is
  begin
    o<=((not a) and (not c) and (not d)) or ((not b) and (not d) and c) or (a and b and (not c)) or (a and b and c);
end operation;

-----**Half Subtractor(Q no:23)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity HalfSubtractor is

  port(

    a,b:in std_logic;--inputs
    difference,borrow:out std_logic);--output

end HalfSubtractor;
--------------------------------
architecture Operation of HalfSubtractor is

  begin

    difference<=a xor b;
    borrow<= (not a)and b;

end Operation;

-----***FullSubtractor(Q no:24)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity FullSubtractor is

  port(

    a,b,c:in std_logic;--inputs
    difference,borrow:out std_logic);--output

end FullSubtractor;
--------------------------------
architecture Operation of FullSubtractor is

  begin

    difference<=((not a) or ((not b) or (not c)))or (a and b and c);
    borrow<= ((not a)and (b or c))or (b and c);

end Operation;

-----***BCD to 7 segment Decoder(Q no:25)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity bcd_7seg_dec is
        port ( w,x,y,z : in std_logic;--inputs
        a,b,c,d,e,f,g: out std_logic);--outputs
end bcd_7seg_dec;
----------------------------------
architecture Operation of bcd_7seg_dec is
begin
   a <= ((not x) and z) or ( x and z ) or ( y and z ) or (w);
   b <= (not x) or ((not y) and (not z)) or (y and z);
   c <= (x) or (not y) or (z);
   d <= ((not x) and (not z)) or (y and (not z)) or ((not x) and y) or (x and (not y) and z);
   e <= ((not x) and (not z)) or (y and (not z));
   f <= (w) or ((not y) and (not z)) or (x and (not y)) or (x and (not z));
   g <= (w) or (x and (not y)) or ((not x) and y) or (y and (not z));
end Operation;

-----***Realization (Q no:27)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Realise3 is
  port(
    a,b,c,d:in std_logic;--inputs
    o:out std_logic);--output
end Realise3;
----------------------------
architecture Operation of Realise3 is
  begin
    o<= ((not a) and (not b)) or (a and b and (not d)) or (a and b and c);
end operation;

-----***2 Bit Comparator(Q no:30)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Comparator is
  port(
    a,b:in std_logic;--inputs
    agb,alb,aeb:out std_logic);--outputs
end Comparator;
------------------------------
architecture Operation of Comparator is

begin
  agb<= a and(not b);
  alb<= (not a) and b;
  aeb<= a xnor b;
end Operation;

-----***4 Bit Comparator(Q no:31)***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity comp_4 is
        port( a,b : in std_logic_vector ( 3 downto 0);--inputs
        aeb,agb,alb : out std_logic);--outputs
end comp_4;
--------------------------------
architecture Operation of comp_4 is
begin
  aeb <= '1' when (a=b) else '0';
  agb <= '1' when (a>b) else '0';
  alb <= '1' when (a<b) else '0';
end Operation;
-----***4-1 Mux Using WithSelect(Q no:32)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
--------------------------------
entity Mux421 is
  port(
    a,b,c,d:in std_logic;--inputs
    s:in std_logic_vector(1 downto 0);
    o:out std_logic);--output
end Mux421;
---------------------------------
Architecture Operation of Mux421 is
begin

  with s select
    o<= a when "00",b when "01",c when "10",d when others;

end Operation;

----***4-1 Mux using When Else(Q no:33)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
--------------------------------
entity MuxWhenElse is
  port(
    a,b,c,d:in std_logic;--inputs
    s:in std_logic_vector(1 downto 0);
    o:out std_logic);--output
end MuxWhenElse;
---------------------------------
Architecture Operation of MuxWhenElse is
begin

    o<= a when s="00" else b when s="01" else c when s="10" else d ;

end Operation;

----***BCD to 7segment using With Select(Q no:34)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
--------------------------------
entity DisplaySelect is
  port(
  -- i:in std_logic;
    s:in std_logic_vector(3 downto 0);--input
    o:out std_logic_vector(6 downto 0)); --output
end DisplaySelect;
---------------------------------
Architecture Operation of DisplaySelect is
begin

  with s select
    o<= "1111110" when "0000",
    "0110000" when "0001",
    "1101101" when "0010",
    "1111001" when "0011",
    "0110011" when "0100",
    "1011011" when "0101",
    "1011111" when "0110",
    "1110000" when "0111",
    "1111111" when "1000",
    "1111011" when "1001",
    "1110111" when "1010",
    "0011111" when "1011",
    "1001110" when "1100",
    "0111101" when "1101",
    "1001111" when "1110",
    "1000111" when others;

end Operation;

-----*** BCD to 7Segment using When Else(Q no:35)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
--------------------------------
entity DisplayWhenElse is
  port(
  -- i:in std_logic;
    s:in std_logic_vector(3 downto 0);--input
    o:out std_logic_vector(6 downto 0));--output
end DisplayWhenElse;
---------------------------------
Architecture Operation of DisplayWhenElse is
begin

    o<= "1111110" when s="0000" else
    "0110000" when s="0001" else
    "1101101" when s="0010" else
    "1111001" when s="0011" else
    "0110011" when s="0100" else
    "1011011" when s="0101" else
    "1011111" when s="0110" else
    "1110000" when s="0111" else
    "1111111" when s="1000" else
    "1111011" when s="1001" else
    "1110111" when s="1010" else
    "0011111" when s="1011" else
    "1001110" when s="1100" else
    "0111101" when s="1101" else
    "1001111" when s="1110" else
    "1000111";

end Operation;

-----***T FlipFlop(Q no:37)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Tflip is
  port(

    t,clk,q0:in std_logic;--input
    q,qbar:out std_logic);--output

  end Tflip;

architecture Operation of Tflip is

  signal qbar1,temp:std_logic;

  begin
    qbar1<= not q0;
    temp<= q0 when clk='1' and t='0' else qbar1 when clk='1' and t='1' else '-';
    q<= temp;
    qbar<= not temp;

end Operation;

-----***D FlipFlop(Q no:38)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Dflip is
  port(

    d,clk:in std_logic;--input & clock
    q:out std_logic);--output

  end Dflip;

architecture Operation of Dflip is

  begin
   q<= d when clk='1' else (not d) when clk='1' and d='1' else '-';

end Operation;

-----***Priority Encoder(Q no:39)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
--------------------------------
entity pr_encod is
  port ( a : in std_logic_vector ( 3 downto 0);
        y : out std_logic_vector ( 1 downto 0 );
        z : out std_logic);
end pr_encod;
--------------------------------
architecture Operation of pr_encod is
  begin
    y<= "11" when a(3)='1' else
        "10" when a(2)='1' else
        "01" when a(1)='1' else
        "00";
    z<= '0' when a="0000" else '1';
end Operation;

-----***Realising 4bit FA with fast carry(Q no:40)***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
use ieee.std_logic_unsigned.all;
------------------------------------
entity FA4bitFC is
  port(
    a_0,a_1,a_2,a_3,b_0,b_1,b_2,b_3,cin:in std_logic;--inputs
    s0,s1,s2,s3,cout:out std_logic);--outputs
end FA4bitFC;
------------------------------------
architecture Operation of FA4bitFC is
signal a: std_logic_vector(1 to 25);
begin
  a(1)<= a_0 nor b_0;
  a(2)<= a_0 nand b_0;
  a(3)<= a_1 nor b_1;
  a(4)<= a_1 nand b_1;
  a(5)<= a_2 nor b_2;
  a(6)<= a_2 nand b_2;
  a(7)<= a_3 nor b_3;
  a(8)<= a_3 nand b_3;
  a(9)<= (not a(1)) and a(2);
  a(10)<= (not cin) and a(2);
  a(11)<= (not cin) and a(4);
  a(12)<= (not cin) and a(2) and a(4);
  a(13)<= a(2) and a(1);
  a(14)<= (not a(5)) and a(6);
  a(15)<= (not cin) and a(2) and a(4) and a(6);
  a(16)<= a(4) and a(6) and a(1);
  a(17)<= a(6) and a(3);
  a(18)<= (not a(7)) and a(8);
  a(19)<= (not cin) and a(2) and a(4) and a(6) and a(8);
  a(20)<= a(4) and a(6) and a(8) and a(1);
  a(21)<= a(8) and a(6) and a(3);
  a(22)<= a(8) and a(5);
  a(23)<= not(a(17) or a(16) or a(15));
  a(24)<= not(a(12) or a(13) or a(3));
  a(25)<= not(a(10) or a(1));
  cout<= not(a(22) or a(21) or a(20) or a(19));
  s0<=a(9) xnor cin;
  s1<=a(25) xnor a(11);
  s2<=a(24) xnor a(14);
  s3<=a(23) xnor a(18);
end Operation;

-----***4 Variable Majority fn(Q no:41)***-----
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity Major4var is
  port(
    a,b,c,d:in std_logic;--input
    o:out std_logic);--output
end Major4var;
----------------------------
architecture Operation of Major4var is
  begin
    o<=(((a and b)) and (d or c)) or(((c and d)) and (b or a));
end Operation;

-----***Traffic Light System(Q no:42)***------
-----coded by Jenson and Salahudheen----

library ieee;
use ieee.std_logic_1164.all;
----------------------------
entity traffic is
  port(
    a,b:in std_logic;--inputs
    r,y,g:out std_logic);--outputs
end traffic;
----------------------------
architecture Operation of Traffic is
begin
  r<=not a;
  y<= b;
  g<= a and (not b);
end operation;